## Slide 1: بسم الله الرحمن الرحیم
Modulator & Power supply
for
High power Microwave Tube
in
LINAc accelerator

## Slide 2: Twystron Tube
Specification:
  S-band (2950-3050 MHz)
  Input RF power : 2kW
  Out put RF Power : 2MW
  PRF: 100Hz
1 RF Input
2 RF output
3 Cathode
4 filament
5 Focus Coil
6 Ion vacuum pump
7 collector
1
2
4
5
7
6
3

## Slide 3: Tube

## Slide 4: Tube

## Slide 5: Driving Assembly Block Diagram
HV Pulsed power Modulator
2KW RF Ass.
Mode Converter
Waveguide
.Focus Coil PS
Vacuum PS
.Pressure Pump
Twystron Tube
Thermionic PS
Coupler
Isolator
Cooling

## Slide 6: Other Tube Power Supply
Parameter | Value
Voltage | 8V
Current | 35A
Mode | DC
Type | SMPS
Filament Power Supply
Focus Coil Power Supply
Parameter | Value
Voltage | 60V
Current | 17A
Mode | DC
Type | SMPS
Vacuum Ion Pump Power Supply
Parameter | Value
Voltage | 3kV
Current | 20mA
Mode | DC
Type | SMPS

## Slide 7: Cooling Assembly
Thermometers
Thermostat
Pressure gauge
Flow controller
Circulation pump
condenser
Filter Ass.
It uses for cooling both isolator and Twystron Tube

## Slide 8: Pressure Assembly
Storage tank
manometer
Circulation pump
Drying ass.
Filter ass.
It uses for pressurizing microwave assemblies after tube

## Slide 9: Microwave Assembly
FPA Output
Isolator
Mode Converter
Waveguide
Cavity
Coupler
2MW RF
TE10
TM01
Pressure Ass.
peak detector
2KW RF input
Disconnection RF Switch

## Slide 10: Microwave Assembly

## Slide 11: Microwave Assembly

## Slide 12: Control System
AC Power
PS control:
  Filament Power Supply
  Focus Coil Power Supply
  Vacuum Ion Pump Power Supply
  Pulsed Power Modulator
RF Reflection control
Cooling Assembly
Pressure Assembly

## Slide 13: HV Modulator specification
Input:
3Ph , 30KVA, 380V ± 15%
Temperature: 0°C ~ 50°C
Humidity: 5% ~ 90% non-condensed
Output:
Filament:
27V/100A, ripple 0.25%, η > 80%, short circuit & Over voltage protection
Focus coil:
270V/12A, ripple 0.25%, η > 80%, short circuit & Over voltage protection
Ion Pump:
3KV/20mA, ripple 0.25%, η > 80%, short circuit & Over voltage protection

## Slide 14
Modulator:
115KV adjustable, 80A
Pulse duration: 2 ~ 7µs adjustable
Pulse rate: 80 ~ 120Hz adjustable
Ripple: 0.25%
η: 80%
Protection:
Short- circuit
Over voltage
Filament power on sequence
Over temperature

## Slide 15: HV Pulsed Power Modulator
parameter | value
Peak voltage | 110kV
duration | 7.5us
Current | 70A
PRF | 100Hz
Low Ripple DC rectifier
Fly Back SMPS 3kV
HV shunt regulator
PF Network
AC&EMI filter ass.
Pulse Trans
Peaking Switch
3ᵠ380v
500VDC
3KV/100Hz
Regulated
3KV/100Hz
1.5KV rectangular wave
110kV/100Hz

## Slide 17: Systems Sections :
Inverter Section
Pulser Section
Output Pulse Transformer
Filament Power Supply
Focus Coil Power Supply
Ion Pump Power Supply
Control Panel

## Slide 18: Systems Sections (Continue)
Inverter Section
  Comprise 6 blocks of Inverter Block
  Each block comprise 5 inverter module
  Each block has a inverter controller

## Slide 19: Inverter Sections (Continue)
Inverter module
  Flyback topology driver
  Transformer with high isolation withstand
  High voltage Isolator for feedback
  Output Rectifier
  Output Filter
  Control Circuit
  Output up to 1KV

## Slide 20: Inverter Sections (Continue)
Inverter module

## Slide 21: Inverter Sections (Continue)
Inverter module

## Slide 22: Inverter Sections (Continue)
Inverter controller
  Input filter
  PFC (Power Factor Corrector)
  Rectifier
  Output : constant HVDC
  Controller
  Interface : 2-way
  Interface 1: with inverter modules
  Interface 2: with control panel

## Slide 23: Inverter Sections (Continue)
Inverter controller

## Slide 24: Inverter Sections (Continue)
Inverter controller power stage

## Slide 25: Inverter Sections (Continue)
Inverter controller

## Slide 26: Inverter Sections (Continue)
Inverter module

## Slide 27: Systems Sections (Continue)
Pulser Module
  IGBT driver
  IGBT device
  Control Circuit
Any IGBT block comprise 5 IGBT module
System consist of 6 IGBT block

## Slide 28: Systems Sections (Continue)
Pulser Module

## Slide 29: Systems Sections (Continue)
Filament Power Supply
  Input filter
  PFC (Power Factor Corrector)
  Rectifier
  Full bridge driver
  Full bridge MOSFET
  Transformer
  Output Rectifier
  Output Filter
  Control Circuit

## Slide 30: Systems Sections (Continue)
Focus Coil Power Supply
  Input filter
  PFC (Power Factor Corrector)
  Rectifier
  Full bridge driver
  Full bridge MOSFET
  Transformer
  Output Rectifier
  Output Filter
  Control Circuit

## Slide 31: Systems Sections (Continue)
Ion Pump Power Supply
  Input filter
  PFC (Power Factor Corrector)
  Rectifier
  Full bridge driver
  Full bridge MOSFET
  Transformer
  Output Rectifier
  Output Filter
  Control Circuit